## Slide 1: Multi-Platform Systems and Options Guide
August 2000

## Slide 2: Introduction
The Compaq StorageWorks Multi-Platform Systems and Options Guide is designed to help customers to match subsystems, software, and components to their requirements. This guide describes the basics of configuring Compaq StorageWorks Fibre Channel RAID Arrays. You will see how to configure the enclosures that hold disk drives, package the enclosures in cabinets, or select pre-packaged subsystems. Then you will be ready to choose operating system platform software for your server(s), and array controller software to support each platform. Finally, you will become familiar with the components needed for a typical SAN configuration.
This edition includes:
  Modular Array (MA) 8000 and Enterprise Modular Array (EMA) 12000
Note: For your convenience, this document contains hyperlinks. To activate this feature, switch to PowerPoint Slide Show view, then double-click the URL you wish to access.

## Slide 3: Options for Ordering MA8000/EMA12000
Predefined Hardware Models
  Predefined hardware configurations
  Mandatory options are controller, ECB, ACS, drives
  Ships fully assembled
Configure to Order
  Customized configuration assembled in the factory
  Requires CTO SKU
  Mandatory options are Cabinet, Controller enclosure, drive enclosures,controller, ECB, ACS, drives
  Ships fully assembled
Loose Piece
  Assembly done on site
  Ships as individual components

## Slide 4: Pre-configured Hardware Packages
MA8000: 175992-B21/B22 (60Hz/50Hz)
  22U Opal Cabinet
  1 Controller Enclosure
  3 Dual Bus, 14 Bay Drive Enclosures
EMA12000 D14: 175990-B21/B22 (60Hz/50Hz)
  42U Opal Cabinet
  3 Controller Enclosures
  9 Dual Bus, 14 Bay Drive Enclosures
EMA12000 S10: 175994-B21/B22 (60Hz/50Hz)
  42U Opal Cabinet
  1 Controller Enclosure
  6 Single Bus, 10 Bay Drive Enclosures
EMA12000 S14: 175991-B21/B22 (60Hz/50Hz)
  36U Opal Cabinet
  1 Controller Enclosure
  6 Single Bus, 14 Bay Drive Enclosures
EMA12000 Blue:175993-B21/B22 (60Hz/50Hz)
  41U Blue Cabinet
  1 Controller Enclosure
  3 Dual Bus, 14 Bay Drive Enclosures
Mandatory Options:
  Controller
  External Cache Battery
  Controller Software
  Disk Drives

## Slide 5: Configure to Order: Combinations of:
Modular Storage Cabinet
  42U, 41U, 36U or 22U
Controller Enclosure
  Model 2200
Drive Enclosures
  Model 4214/4254
  Model 4314/4354
  Model 4310/4350
Controller
  HSG80 (256 MB cache)
Controller Software
  ACS 8.5G
  ACS 8.5F
  ACS 8.5S
  ACS 8.5P
Disk Drives
  9 GB 1”
  18GB 1”
  36GB 1”
  72GB 1.6” (for use with 10 bay 4310/4350 enclosures only)
REQUIRES CTO PART NUMBER: 118102-888

## Slide 6: MA8000 and EMA12000
Fibre Channel Arbitrated Loop uses Fibre Channel hubs
Fibre Channel Arbitrated Loop Platforms Supported:
  Windows NT/x86/Alpha/2000
  Novell NetWare
  SGI IRIX
  IBM AIX
  HP-UX
  Sun Solaris
  Linux
Fibre Channel Switched Fabric uses Fibre Channel switches
Fibre Channel Switched Fabric Platforms Supported:
  Windows NT/x86/2000
  OpenVMS
  Tru64 UNIX
  HP-UX (via QuikLoop)
  Sun Solaris

## Slide 7: MA8000 / EMA12000 Building Blocks: Model 2200 Controller Enclosure
Includes:
redundant power supplies
redundant cooling
Environmental Monitoring Unit
Storage Controllers*
176622-B21 HSG80 Controller with 256MB Cache
*Note: Always choose the same amount of cache for both controllers in a pair
Options:
One or two storage controllers* with 256MB cache
Cache expansion to 512MB
External Cache Battery (one per controller)
Cache
380674-B21 256MB Cache for HSG80 Controller
Cache Batteries
380566-B21 Single Cache Battery

## Slide 8: MA8000 / EMA12000 Building Blocks: Model 4200 and 4300 14 Bay Enclosures
4214R (103381-001, B31, 291)
4314R (190209-001, B31, 291)
Both Include:
Single power supply
Single Bus I/O
redundant cooling
Environmental Monitoring Unit
4254R (138151-001, B31, 291)
4354R (190211-001, B31, 291)
Both Include:
Dual Power supplies
Dual Bus I/O
redundant cooling
Environmental Monitoring Unit
Enclosure Options
4214R Redundant Power Supply: 119826-B21
Ultra 2 Dual Bus I/O: 119829-B21
Ultra3 Single Bus I/O Module: 190212-B21
Ultra3 Dual Bus I/0 Module: 190213-B21

## Slide 9: MA8000 / EMA12000 Building Blocks: Model 4310 and 4350 10 Bay Enclosures
4310R (174631-B21) Single Bus
4350R (174630-B21) Dual Bus
Both Include:
Dual Power supplies
redundant cooling
Environmental Monitoring Unit
Enclosure Options
Ultra3 Single Bus I/O Module: 190212-B21
Ultra3 Dual Bus I/0 Module: 190213-B21

## Slide 10: Cabinetry to Fit Your Environment
Modular Storage Cabinets
Includes dual PDU, power cables, filler panels
Part Numbers:
180311-B21: Modular Storage Cabinet 42U Opal 60Hz
180312-B22: Modular Storage Cabinet 42U Opal 50 Hz
180313-B21: Modular Storage Cabinet 36U Opal 60Hz
180314-B22: Modular Storage Cabinet 36U Opal 50Hz
180315-B21: Modular Storage Cabinet 22U Opal 60Hz
180316-B22: Modular Storage Cabinet 22U Opal 50Hz
180317-B21: Modular Storage Cabinet 41U Blue 60Hz
180318-B22: Modular Storage Cabinet 41U Blue 50Hz

## Slide 11: Disk Drives: MA8000 and EMA12000
Select drives as required to fill available slots, and onsite spares as needed
1” Universal Drive Carrier
1.6” Drive Carrier
*The 0.6” drive extender required for use in these drive enclosures.

## Slide 12: Fibre Channel Operating System Software
Select one Software Kit per operating system and one Fibre Channel Adapter per host connection
* Order from vendor supplier

## Slide 13: Fibre Channel Storage Area Network (SAN) Components

## Slide 14: Part Number Summary: Hardware Packages

## Slide 15: Part Number Summary: Hardware

## Slide 16: Part Number Summary: Software